## Slide 1
Angle-domain Wave-equation
Reflection Traveltime Inversion
Sanzong Zhang, Yi Luo and Gerard Schuster
(1) KAUST, (2) Aramco
1
1
2
Notes: Good afternoon, everyone. The title of my talk is wave-equation reflection traveltime inversion. The coauthors are Dr. Yi Luo from Aramco, and Prof. Schuster.

## Slide 2
Outline
Introduction
Theory and method
Numerical examples
Conclusions

## Slide 3
Outline
Introduction
Theory and method
Numerical examples
Conclusions

## Slide 4
Velocity Inversion Methods
Data space
Image space
Ray-based tomography
Full Waveform inversion
Ray-based MVA
Wave-equ. MVA
Inversion
(Tomography)
(MVA)
Wave-equ. Reflection traveltime inversion
Wave-equ. Reflection traveltime inversion
Notes: The current velocity inversion methods can be divided into two types. One type defines the objective function in data space, such as traveltime tomography and full waveform inversion. The other type defines the objective function in model space, such as ray-based MVA and wave-equation-based MVA.

## Slide 5
Problem
-
2
e =
Pred. data – Obs. data
Model Parameter
The waveform (image) residual is highly nonlinear with respect to velocity change.
The traveltime misfit function enjoys a somewhat linear relationship with velocity change.

## Slide 6
Angle-domain Wave-equation
Reflection Traveltime Inversion
Traveltime inversion without high-frequency approximation
Misfit function somewhat linear with respect to velocity perturbation.
Wave-equation inversion less sensitive to amplitude
Multi-arrival traveltime inversion
Beam-based reflection traveltime inversion
Notes: To exploit the strengths and avoid the weaknesses of both traveltime tomography and full waveform inversion, wave-equation-based transimission traveltime inversion was developed to invert the velocity model. This method tried to invert the transmission traveltime informaiton using the method similar to full waveform inversion.

## Slide 7
Outline
Introduction
Theory and method
Numerical examples
Conclusions

## Slide 8
Wave-equation Transmission
Traveltime Inversion
1). Observed data
5
0
Time (s)
4). Smear time delay
along wavepath
2). Calculated data
0
Time (s)
5
-1.5
1.5
0
Lag time (s)
3).
Notes: For transmission tomography, the receiver records the first arrival initiated by the source. The misfit function is defined to minimize the traveltime difference between the observed data and the calculated data. This misfit function is similar to that of ray-based traveltime tomography.

## Slide 9
Angle-domain Wave-equation
Reflection Traveltime Inversion
Suboffset-domain crosscorrelation function :
)
:
: time shift
g
s
x
x-h
x+h

## Slide 10
Angle-domain CIG decomposition (slant stack ):
angle-domain
suboffset-domain
Angle-domain crosscorrelation function :
)
Angle-domain Crosscorrelation

## Slide 11
Angle-domain Crosscorrelation:
physical meaning
)
Angle-domain crosscorrelation is the crosscorrelation
between downgoing and upgoing beams with a certain angle.
The time delay for multi-arrivals is available in angle
-domain crosscorrelation function .
)
Local plane wave
)
Local plane wave

## Slide 12
Angle-domain Wave-equation Reflection Traveltime Inversion
Objective function:
Velocity update:
(x)= (x) + (x)
Gradient function:
Traveltime wavepath

## Slide 13
Traveltime Wavepath
Angle-domain time delay
Angle-domain connective function
Traveltime wavepath

## Slide 14
Transforming CSG Data  Xwell Trans. Data
=
+
reflection
transmission
transmission
Src-side Xwell Data
Redatuming data
source
Redatuming source
Observed data
Rec-side Xwell Data

## Slide 15
Forward propagate source to trial image points and get downgoing beams
Backward propagate observed reflection data from geophonses to trial image points , and get upgoing beams
Crosscorrelate downgoing beam and upgoing beam, and pick angle-domain time delay
Workflow
Smear time dealy along wavepath to update velocity model

## Slide 16
Introduction
Theory and method
Numerical examples
Simple Salt Model
Sigsbee Salt Model
Conclusions
Outline

## Slide 17
Simple Salt Model
0
4
0
8
(a) True velocity model
x (km)
z (km)
0
8
x (km)
0
5
(b) CSG
t (s)
1
5
V(km/s)
0
4
0
8
(c) Initial Velocity Model
x (km)
z (km)
0
4
0
8
(d) RTM image
x (km)
z (km)

## Slide 18: Angle-domain Crosscorrelation
0
4
0
8
(a) Initial Velocity Model
x (km)
z (km)
(b) Angle-domain Crosscorrelation
(c) Angle-domain Crosscorrelation
time delay
curvature
reflection angle

## Slide 19
Inversion Result
0
4
0
8
(a) Initial velocity model
x (km)
z (km)
0
4
(b) Inverted velocity model
z (km)
0
8
x (km)
1
5
Velocity(km/s)

## Slide 20
Inversion Result
0
4
(b) RTM image
z (km)
0
8
x (km)
0
4
0
8
(a) RTM image
x (km)
z (km)

## Slide 21
Introduction
Theory and method
Numerical examples
Simple Salt Model
Sigsbee Salt Model
Conclusions
Outline

## Slide 22: Sigsbee Model
Vinitial = 0.85 Vtrue
0
6
0
12
z(km)
x(km)
0
6
0
12
z(km)
x(km)
1.5
4.5
Velocity (km/s)
(a) True velocity model
(b) Initial velocity model
0
6
0
12
z(km)
x(km)
(c) RTM image

## Slide 23: Initial Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
-0.2
0.2

## Slide 24: Initial Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
-0.2
0.2

## Slide 25: Initial Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
0.2
-0.2

## Slide 26: Inverted Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
-0.2
0.2

## Slide 27: Inverted Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
-0.2
0.2

## Slide 28: Inverted Velocity Model
0
6
0
12
z(km)
x(km)
0
6
-50°
+50°
CIG
-0.04
0.04
z(km)
Crosscorrelation
-50°
+50°
0
6
z(km)
Semblance
-0.2
0.2

## Slide 29: RTM Image
0
6
0
12
z(km)
x(km)
(a) RTM image using initial velocity
0
6
0
12
z(km)
x(km)
(b) RTM image using inverted model

## Slide 30
Outline
Introduction
Theory and method
Numerical examples
Conclusions

## Slide 31
Velocity Inversion Methods
Data space
Image space
Ray-based tomography
Full Wavform inversion
Ray-based MVA
Wave-equ. MVA
Inversion
(Tomography)
(MVA)
Wave-equ. traveltime
inversion
Wave-equ. traveltime
inversion
Notes: The current velocity inversion methods can be divided into two types. One type defines the objective function in data space, such as traveltime tomography and full waveform inversion. The other type defines the objective function in model space, such as ray-based MVA and wave-equation-based MVA.

## Slide 32
Angle-domain Wave-equation
Reflection Traveltime Inversion
Traveltime inversion without high-frequency approximation
Misfit function somewhat linear with respect to velocity perturbation.
Wave-equation inversion less sensitive to amplitude
Multi-arrival traveltime inversion
Beam-based reflection traveltime inversion
Notes: To exploit the strengths and avoid the weaknesses of both traveltime tomography and full waveform inversion, wave-equation-based transimission traveltime inversion was developed to invert the velocity model. This method tried to invert the transmission traveltime informaiton using the method similar to full waveform inversion.

## Slide 33
Thank you for your attention